Dear Dr. Case,
I have read your tutorial on thermodynamic integration (TI) and I was performing the same calculation (Tolune---> nothing) in the tutorial given. But unfortunately I got some differnt results as compared to the tutorial. 

First of all I created the  prmtop.coul.vac and prmcrd.coul.vac files from Xleap. Then I used these files to run for a charging free energy calculation in vaccum and interestingly I got almost same result of DV/DL (-0.4625) compared to tutorial DV/DL ( -0.4646). Then I created the prmtop.coul.wat and prmcrd.coul.wat files for the charging free energy calculation in water. I used the same input files as given in the tutorial for both equilibration and production part with three different values of clambda (0.11270, 0.5 & 0.88729) and finally I got the more or less same results as follows:

| clambda | DV/DL from my calculation | DV/DL from tutorial |
| --- | --- | --- |
| 0.11270 | 4.4439 +/- 2.1355 | 4.13 +/- 2.26 |
| 0.5 | 1.5345 +/- 1.7721 | 1.52 +/- 1.80 |
| 0.88729 | -0.3335 +/- 1.42 | -0.26 +/- 1.49 |

So my question is that if I am using the same input as per the tutorial and also the same prmtop & prmcrd files , why this difference in results is coming??

Secondly I also tried for the Disappearing free energy calculation for both  in vaccum and in water. For vaccum part I got the DV/DL  of  -1.8537 . the input for the vaccum is as follows:

Here is the input file:
                                                                                                                             
neutralize toluene
 &cntrl
 ntr=0,
 nstlim =100000, nscm=2000, ntave=10000,
 ntx=5, irest=1, ntb=0, ntpr=200,
 ntp=0, taup=2.0,
 dt=0.001, nrespa=2,
 ntt=1, temp0=300., tautp=2.0,
 ntc=2, ntf=2, tol=0.000001,
 ntwr = 10000, ntwx=0,
 icfe=1, klambda=4,
 cut=9.0,
&end


For disappearing free energy calculation in water part I equilibrated the system for each individual values of clambda and then run for the production for the same value of clambda. I used five values of clambda from 0.05, 0.15,0.25, 0.35 and 0.45 with klambda =4. Here is my result which is far different from the results of your tutorial.

| clambda | DV/DL from my calculation |
| --- | --- |
| 0.05 | 13.2628 |
| 0.15 | 4.1287 |
| 0.25 | 1.3485 |
| 0.35 | 0.0854 |
| 0.45 | -0.0716 |

Here is an  input file for an example for clambda = 0.05
                                                                                                                             
neutralize toluene
&cntrl
 ntr=0,
 nstlim =100000, nscm=2000, ntave=5000,
 ntx=7, irest=1, ntb=1, ntpr=100,
 ntp=0, taup=2.0,
 dt=0.001, nrespa=2,
 ntt=0, temp0 = 300., tautp=2.0,
 ntc=2, ntf=2, tol=0.000001,
 ntwr = 10000, ntwx=0,
 icfe=1, clambda=0.05, klambda=4,
 cut=9.0,
&end

I am using the AMBER-8 version in a Linux system. 
So can you  please point out the reason of differnce in results and also the mistake.

With regards
Biswa Ranjan Meher