## Slide 1: What is an assignment?
Associate a given signal back to the originating spin

## Slide 2: Every atom with spin has a Larmor frequency
Fourier Transform (FT)
Time  Frequency
‘X’ Hz
‘Y’ Hz
This frequency is a physical property of that atom – it is the same value no matter what experiment is run!
Assignments!

## Slide 3: Homonuclear 2D Expts

## Slide 4: Double-Resonance Experiments Increases Resolution/Information Content
15N-1H HSQC

## Slide 5: Basic Strategy to Assign Resonances
Identify resonances for each residue (scalar)
Put residues in order
1 2 3 4 5 6 7
R - G - S - T - L - G - S
L
T
G
S
S
R
G

## Slide 6: Heteronuclear Triple-Resonance Backbone Experiments
Names of scalar experiments based on atoms detected

## Slide 7: Topics for today:
Sequential walking
Mapping spin systems to the protein sequence
Choosing the right triple resonance experiment
Tricks for resolving challenging systems
  (What to do when the CBCACONH doesn’t cut it!)
Translating assignments to a protein complex
Software packages for spectra visualization
Basic primer of the hands-on tutorial
Using the software: the assignment process demo

## Slide 8: Protein Backbone Assignment
A
B
C
1H
15N

## Slide 9: Connecting Spin Systems
A
B
C
13C
1H
15N
BAC

## Slide 10: Strip Matching View
13C
1H
15N
C
D
E
F
G
H
I
Pseudo-
Residue:

## Slide 11: Turning Pseudo-residues to Assignments
Problem:
Need a to convert strips to sequence
Solution:
Determine amino acid identity
Compare to known protein sequence

## Slide 13: Unique spins of some residue types
Alanine
  High alpha (52)
  Unique beta (19)
Glycine
  Unique alpha (45)
  No beta
Proline
  No direct signal (no HN)
  Can still observe (i-1) signal
Serine/Threonine
  Unique betas (63/69)
Asparagine/Aspartate
  High alpha & Low beta
Isoleucine
  Low alpha and low beta
Valine
  Low alpha and high beta

## Slide 14: Example Assignment
RERRIHVTQEDFELAVGKVMNKNQETAISVAKLFK

## Slide 15: All Spins Need to “Walk”
Cross-validate assignments – all spin types will walk if assignments are correct!
Redundant data is safer!

## Slide 16: Techniques to interpret tricky assignments

## Slide 17: Selective Amino Acid Labeling
Create selectively labeled sample
Acquire HSQC/TROSY
Identify spin systems of labeled type
1 type
19 types

## Slide 18: Secondary Structure Influences Chemical Environment

## Slide 19: Secondary Structure Influences Carbon Chemical Shifts
If secondary structure is known (i.e. homology model or structure), one can anticipate shifting from the literature random coil value.
↑ : β-strand
‒ : unstructured
↓ : α-helix

## Slide 20: Moving back to Homonuclear
15N-dispersed 3D homonuclear expts – relates side chains to amides
15N-NOESY has signals unique to 2° - useful for linking pseudo-residues in a helix
  i.e. α-helicies have i to i+3/i+4 NOE’s
15N-TOCSY or NOESY shows number of hydrogens in a side chain – useful for amino acid type identity

## Slide 21: Practical Considerations
The best way to get good assignments it to collect good data!

## Slide 22: Sample Preparation
Target 400-600 μM concentration
  2x conc = 4x sensitivity
15N-13C labeled (~90% 2H preferred)
  Deuterium slows relaxation, more signal
Stable for ~4-6 days in acquisition buffer
  Minimal precipitation/aggregation
  Sometimes concentration dependent
Hydrated in water-based buffers (not D2O or organics) to have signal.
Salt below 100 mM to take advantage of cryoprobe sensitivity

## Slide 23: Spectra Sensitivity
Approximate relative sensitivity:
HNCO
HNCOCA
HNCA
HNCACB
HNCACO
CBCACONH
Non-Uniform sampling (acquire ~25% of points)
CACB pair gives most data/connectivities, but is least sensitive.
CA pair is generally more useful than CO pair for connectivities
More sensitive
Less sensitive

## Slide 24: Spectral Resolution
HNCO good for determining if H-N peaks are overlapped.
HNCA has better resolution than HNCACB, good dispersion and smaller frequency range

## Slide 25: Choosing what spectra to acquire
Know what assignments you need:
  Assign HSQC, full backbone, or complete assignment?
Always start and end acquisition with a 15N-HSQC
  Checks for protein folding/degradation & sensitivity changes
H-C plane projections (set 15N resolution to 1)
  Quick way to see if there is good enough sensitivity before 3D
  Always test CACB sensitivity first – usually preferred if good sample

## Slide 26: Assignment of a Protein Complex

## Slide 27: Assignments of a Protein-ligand Complex
Sometimes free and bound spectra are significantly different:
Re-assign backbone with triple resonance
Translate spin system assignments from free to bound state using amides as a proxy

## Slide 28: Interactions: Equilibrium time scale
slow
intermediate
fast
Keq
δA
δB
[A] ≈ [B]

## Slide 29: Interactions: Fast Exchange
slow
intermediate
fast
Keq
δA
δB
[A] ≈ [B]

## Slide 30: Interactions: Slow Exchange
slow
intermediate
fast
Keq
δA
δB
[A] ≈ [B]

## Slide 31: ZZ-Exchange correlations
Tight interactions (nM dissociation)
Subsaturating ligand creates two states in slow exchange
Translate assignment from free state to bound state by identifying cross peaks

## Slide 32: Intro to the Assignment Tutorial

## Slide 33: The Ubiquitin Proteasome System

## Slide 34: Introduction to Ubiquitin
MQIFVKTLTGKTITLEVEPSDTIENVKAKIQDKEGIPPD QQRLIFAGKQLEDGRTLSDYNIQKESTLHLVLRLRGG
76 amino acids
~8.5 kDa
Strong/dispersed signal

## Slide 35: What are we doing next class?
Pair into groups of two – meet here to start class
Find a workstation
Assign the backbone of ubiquitin
  15N-HSQC
  CBCACONH
  HNCACB
Learn visualization software

## Slide 36: Visualization Software
Sparky
NMR ViewJ
XEASY
CARA
CCPNMR

## Slide 37: The Complete Assignment Process
View HSQC
Generate (pick) peaks on HN correlations
Look into carbon plane for each given H and N ppm
Pick peaks for each carbon resonance
Use overlays to determine i and i-1
Sequential walking
Amino acid type identification
Map strip series to sequence
Verify assignments with every acquired spectrum
Determine side chain assignments, if necessary.

## Slide 38: Demonstration